H805SB INSTRUCTIONS

Ⅰ.Introduction

H805SB is a LED controller that is capable of controlling a variety of single or double-line driver chips with one port and has infrared remote control and nixie tube display functions. The maximum clock frequency of H805SB is 2.0 MHZ and can control maximum 4096 pixels.

Auxiliary software is “LED Build Software”.

Ⅱ.Controllable Driver Chips

LPD6803, LPD8806, LPD6813, LPD1882, LPD1889, LPD6812, LPD1883, LPD1886, DMX512, HDMX, APA102, UCS6909, UCS6912, UCS1903, UCS1909, UCS1912, WS2801, WS2803, WS2811, WS2812, TM1803, TM1804, TM1809, TM1829, TM1812, TA9912, TM1913, TM1914, TM1916, TM1926, SM16711, INK1003, LX1003, LX2003, LX2006, TLS3001, TLS3002, DZ2809, P9813, P9816, SM16716, LD151x, LD153x, MBI6021, MBI6023, MBI6024, etc.

The type of LED driver chip must be set in software; the same time-sequence driver chips share an option. The type of driver chip only displays a representative name in computer property.

Ⅲ.Performance

1. With only one output port, control maximum 4096 pixels.

2. SD card supports FAT32 and FAT16 format, the maximum capacity is 32G bytes, stores maximum 64 DAT files, which are played based on file name in alphabetical order.

3. With infrared remote control and nixie tube display functions.

4. Can switch files, adjust brightness, set clock frequency and play speed.

Ⅳ. Remote control Operations

- Switch DAT file:

Press “file” to enter DAT mode, nixie tube will display the DAT file number. Press “+” or “－” to switch to the next file or the previous file; You can still use the digital keys to enter the DAT file name you want to play and press “confirm” to switch to the file.

- Set the clock frequency:

Press “clock” to display the current clock, which includes an integer part and a decimal part, the unit is MHZ. You can change the clock by pressing “+” and “－”, can also set the clock by using the digital keys, then press “confirm” to confirm.

- Set play speed:

Play speed ranges from 1 to 200, the unit is frame per second. Enter the setting value with digital keys, press “confirm” to confirm and save, can also use “+”, “－”keys to set.

- Set the brightness:

The value of brightness ranges from 1 to 31, it only works for those chips that support brightness adjustment (LPD6803&LPD8806 don’t support brightness adjustment). Enter the brightness value with digital keys, press “confirm” to confirm and save, can also use “+”, “－”keys to set.

- Playing File selection

H805SB defaults to playing the files in SD card recurrently, you can choose to play single file continuously.

“All Playback” is continuously playing all DAT files in cycle.

"Select Playback" is playing a single DAT file.

- Color modulation

Press “Select” to enter color modulation mode, then press “selection” to adjust the brightness of blue, press “select playback” to adjust the brightness of green, and press “all playback” to adjust the brightness of red. Particularly, LPD6803 and LPD8806 don’t support color modulation function.

Ⅴ.Operation Instructions

- The nixie tube displays “05” after power-on; the right point will                 keep flashing if not insert SD card. Displays “FE” on nixie tube means the DAT file is wrong or too many pixels, for instance, the control type is wrong. The nixie tube displays the file number “01” if read SD card successfully.

- SD card must be formatted into FAT32 or FAT16 after first time use. H805SB supports SDHC (high capacity SD card), the maximum capacity is 32G. SD card can store maximum 64 DAT files, which are played based on file name in alphabetical order.

- In “LED Build Software”, select “one line with a slave”, the controller type must select SB and the chip type must be selected properly.

- The clock frequency and speed are set in controller. Normally, set the clock frequency at 1MHZ, set speed at 25 frames per second

Ⅵ.Ports Definition

Connect GND, DAT when control single-line driver chip

Connect GND, CLK, DAT when control double-line driver chip

Connect GND, D-, and D+ when control DMX512

# Ⅶ. Specifications

| Input Voltage | DC5-24V |
| --- | --- |
| Power Consumption | 1W |
| Drive pixels | 4096 |
| Weight | 40g |
| Working Temperature | -20C°--75C° |
| Dimension | L70 x W45 x H19 |